Traffic Lights

The traffic lights are laid out in such a manner that there are 5 lights per direction. Three LEDs (R, Y, G) are the vehicle lights, and two LEDs (R & G) are pedestrian.

Lights 1, 2 & 3 are for traffic travelling E to W.

Lights 6, 7, & 8 are for traffic travelling S to N.

Lights 11, 12 & 13 are for traffic travelling W to E.

Lights 16, 17 & 18 are for traffic travelling N to S.

North/South should be your main street. East/West should be your side street.

The pin numbers correspond to the LED labeled with that number.

The two rightmost pins are GND  (only one needs to be connected) and the two pins next to those are Vcc (+5V) (only one needs to be connected). Make sure the Vcc for the traffic lights and your board are tied together, and make sure the GNDs for  the traffic lights and your board are tied together as well.

The LEDs will always be on unless they are tied LOW, or receive a LOW signal from your board.

To test each LED, connect power and ground and turn the power on. Connect a wire from GND to each pin consecutively ensuring each turns off.