Programming style tips

Good coding requires fewer comments

Tip1:

Use different naming conventions for constants and variables.

MY_CONST	=0x77	; a constant, defined by me

;all upper case

my_var			;a variable defined by me

;lower case

myFunction		;a function defined by me

;camel case

This way I can immediately identify anything. (Like colour coding wiring in a circuit.)

Tip2:

Eliminate magic numbers by using constants for bit numbers.

sendToDevice(34)

is not as useful as

sendToDevice(PARAMETER_A+PARAMETER_B)

following

;device definitions

PARAMETER_A =32

PARAMETER_B =2

PARAMETER_C =1

etc.

Also, easier to search code for “_PARAMETER_A” than “32”.

Tip2a:

Use constants for configuration bits to clarify configuration.

This is useful for all kinds of configuration bits, (including external devices), and it's even useful when having a bit CLEARED (ie. zero) has some function.

;DAC configuration  options

DAC_LOAD_B=2

DAC_SHUTDOWN_A=0x30

DAC_NO_OPERATION=0x20

sendToDevice(DAC_LOAD_B + DAC_SHUTDOWN_A, data )

Obviously no comment is needed for the previous line,

and if you changed it to

sendToDevice(DAC_LOAD_A + DAC_SHUTDOWN_B, data )

you wouldn't need to notice the comment was incorrect and change it.

Tip2b:

Start all definitions for specific devices with a common prefix.

;DAC definitions

DAC_LOAD_B=2

;LCD display options

LCD_DISPLAY_ON=4

;LCD functions

LCDSendChar

etc.

Then you can search for everything related to a device or function easily.